## Slide 1: Immunoassay Results
Qualitative
  Single point calibration at a specific cut off
  Results are either ‘positive’ or ‘negative’; (i.e. above or below the cut off)
  Possible false positives; monoclonal antibodies restrict this slightly.
Quantitative
  Provides numeric results that are an estimate of drug/compound concentration based on the measurement of labeled analyte in the solution, and taking into consideration the competitive/noncompetitive nature of the device.
  In terms of use on drugs, this is sometimes complicated by possible cross-reactivities.

## Slide 2: Immunoassay Results Cont’d
Typical 4-parameter logistic graph for a competitive-format immunoassay.
Dose-response curve for a non-competitive CL immunoassay.
A pregnancy test is an example of a commercially produced immunoassay that produces a positive or negative qualitative response.

## Slide 3: Immunochromatography test strip to measure Digoxin
Preparation of Digoxin–Protein Conjugates
Synthesis of colloidal gold
Preparation of colloidal gold probe
Characterization of the probe
Preparation of immunochromatography test strip

## Slide 4
Add Sample
Conjugate
Control
line
Test
Line
Digoxin
Anti-IgG/gold
antibodies
Dig-BSA
Colloidal gold
conjugated to Dig antibodies

## Slide 5
Negative
Digoxin
Colloidal gold
conjugated to Dig antibodies
Dig-BSA
Control
line
Test
Line
Digoxin
Colloidal gold
conjugated to Dig antibodies
Anti-IgG/gold
antibodies
Dig-BSA
Positive

## Slide 6
IMMUNOSENSORS

## Slide 7: Immunosensor
Immunosensors are biosensors which use antibodies as selective recognition elements.
These antibodies are immobilized on to the surface
The binding reversible event (antibody to antigen) is then transformed into measurable signal by the transducer, which builds a measurement unit with the recognition device.

## Slide 8
Ab/Ag interaction is specific and reversible (non-covalent interactions)
Biomolecular interactions can be classified in tdifferent categories, according to the test format performed (i.e., direct and indirect (sandwich or Noncompetitive) and competitive ).

## Slide 9
Direct Biomolecular interactions
In a direct format the immobilized target molecule interacts with a ligand molecule or the immobilized ligand interacts with a target molecule directly.
The sensitivity obtained when using these techniques increases with increasing amounts of immobilized receptor.

## Slide 10
Indirect Biomolecular interactions

## Slide 11
Competitive Biomolecular interactions
The indirect format involves competition between labeled and unlabeled antigens.
In this case, the unlabeled analyte competes with the labeled analyte for a limited number of receptor binding sites.
Assay sensitivity therefore increases with decreasing amounts of immobilized reagent.

## Slide 12
Immunosensores classification based on labeling
Labeled immunosensoring:
radioisotope, enzyme, fluorescents, chemiluminescent .
Unlabeled immunosensoring:
The formation of the Ag/Ab complex in directly measured by an optical or electrical or piezoelectric changes in matrix.
It saves time and it has fewer step as well.

## Slide 13
In the case of HRP, the substrate is hydrogen peroxidase and the redox mediator must be an adequate electron donor (a reduced species such as hydroquinone).
HRP enzymatic activity converts the reduced redox mediator (hydroquinone) into an oxidized one (benzoquinone), which is further electrochemically reduced at the electrode surface.
Examples of
Electrochemical Immunosensor

## Slide 14
Blocked Electrochemical Sensor Technology (BEST)
using molecules as wires to allow electrochemical communication with an electrode.
modifying an electrode surface with a molecular wire and an insulator component.
To the end of the molecular wire is attached a redox probe and an antigen.
An antibody for this antigen will specifically bind to the electrode surface.

## Slide 15
When this happens the electrochemistry from the redox probe is suppressed. If the sensor is exposed to a sample containing the antigen, the antibody will dissociate from the surface to bind with the antigen in a competition for the antibody between solution and surface bound antigen in solution and gives an increase in electrochemical current.

## Slide 16
The electrode can be modified such that nonspecific adsorption of proteins to the electrode surface are restricted.
A label free immunosensor for the detection of small molecules such as pesticides and drugs.
Molecular wires which penetrate the insulator layer, allow electrical communication to the underlying electrode.
Also attached to the redox active species can be an analogue of the antigen.
The advantages of this strategy